## Slide 1: Neural Semiconductor Limited Seamless Technology Service
Project Report of cv32e40p Block
Name : Khairul Alam Johny
Associate Physical Design Engineer (Trainee)

## Slide 2
CONTENTS
DESIGN SUMMARY
SYNTHESIS
FLOORPLAN
ROUTING
PLACEMENT
CLOCK TREE SYNTHESIS
SETUP & HOLD TIMING FIXED
POSTROUTE
DESIGN RULE CHECK
02
Notes: Today I will be looking over these topic from my project starting from design summary all the way to design rule

## Slide 3
Design Summary
DESIGN FLOW & SPECIFICATION |  |  |  |  |  | 
FLOW | SYNTHESIS | FLOORPLAN | PLACEMENT | CTS | ROUTING | POSTROUTE
SPECIFICATION | Frequency - 450MHz Synthesis VT cell – HVT & RVT Physical synthesis - Required | Area ratio – 0.7 Shape After floorplan utilization – 95% Power stripe 15% to 20% | 2nd highest instance module fixed in a specified core boundary area | NDR rule 2x space 3x width -- Top rule 2x space 2x width -- Trunk-- Shield Apply rule 2x space 1x width – leaf Check if the uncertainty if set properly if not find the root cause and fix it. (10% of clock period) Check if the clock is propagated or ideal if ideal find root cause make the clock tree propagated | Detouring off Routing congestion high used partial blockage | Setup time and hold time fixing DRC fixing DRV fixing
03
Notes: Here we can see the design flow and specifications that are required for my design. Here the design flow are from synthesis to postroute and Given some specifications for synthesis

## Slide 4
SYNTHESIS
Input Files
RTL
Constraints file (.sdc)
Lib file
Netlist
SDC
Reports
Output Files
Period 2.22ns
Waveform 0 to 1.11ns
Uncertainty 0.222ns (10%)
SDC Modification
syn_generic
Converting RTL into simple logic gates.
syn_map
Mapping gates to actual technology-dependent logic gates
syn_opt
Optimizing the mapped netlist.
04
Report of Results | 
Total cell | 17586
Cell area | 54069.174 um2
Total Area | 77019.492 um2
Setup Time | reg2reg (0.0)ps wns
The process of translating the RTL into a gate-level netlist is called Synthesis. There are two type of synthesis.
1. Logical synthesis
2. Physical synthesis.
Notes: I was changing sdc modification for my design specification period was 2.22ns waveform was 0 to 1.11ns.uncertainty was 0.222ns which is 10% of period. The process of genus synthesis is done in 3 main steps. then I get some output files. here we can see the report of results after the synthesis is done.

## Slide 5
Physical Synthesis
RTL
SDC
Lib files
DEF and LEF files
05
Fig : syn_generic log file
Physical synthesis begins with a mapped netlist generated by logic synthesis. The netlist describes the logical connections among the physical components (logic gates, macro, I/O pins, etc.). Physical synthesis generates a new optimized netlist and a corresponding layout.
Input Files
1
0
Synthesis
Logical Synthesis
Physical Synthesis
syn_physical_opt
syn_generic -physical
Notes: Logical synthesis is done after using data in physical synthesis and When is used physical information from design impelementation I set the syn_phy_opt to 1 which initial syn_gen –physical proceedes to take the read lef and read def but due to unavailibity of the license phy syn can not take place

## Slide 6
Floorplan & Powerplan
06
sroute
Die boundary
Core boundary
Metal5
Metal4
Floorplan |  |  | 
Core width |  | 285.57um | 
Core height |  | 200.64um | 
Core to die width |  | 10.26um | 
Core to die height |  | 9.12um | 
Powerplan |  |  | 
Layer name | Top power layer |  | Bottom power layer
Metal Number | Metal 5 |  | Metal4
VDD width | 2 |  | 1.8
VSS width | 2 |  | 1.8
Set to set distance | 23.58 |  | 19.86
Number of stripe | 9 |  | 15
Percentage of power stripe | 18% |  | 18.9%
Floorplan creates die boundary and core boundary . It is also a process of positioning blocks or macros on the core boundary.
Fig : Floorplan & Powerplan
create_floorplan -core_size
add_stripe
command
Notes: Floorplanning die and core area has to be fixed before placing the std cell .this is the picture of the floorplan stage of my project. I used some parameters for floorplaning and powerplaning.i set core and die boundary. Top Power routing I used metal5 which is hor and bottom power routing metal4 which is vertical. Create_floorplan –core_size this cammand is used for floorplaning and add_strips

## Slide 7
Floorplan & IO placement
07
Pin connection | 
Module name | Position
id_stage_i | half of bottom side pin
load_store_unit_i | right side pin
if_stage_i | left side pin
cs_register_i | half of bottom side pin
After Floorplan check reports | 
Verify command | Comments
check_pin_assignment | Total 379 number of pin is legal
check_place | Place cell 282 Unplace cell 18318 Utilization density is 95.36%
check_pg_short | Zero violations
Setup time | -0.773ns (wns) reg to reg
IO file command
write_io_file cv32e40p_top.io
read_io_file cv32e40p_top.io
Fig : Pin connection
Notes: In order to make my pin management optimized I tried to keep all the pin associate to certaint module in one side that the picture have mentioned and dumped io script using write_io. then I verified some ascpect after floorplan stage .My recomendation is 95% density after floorplan I have done it

## Slide 8
Fig : ex_stage_i – fixed module
Boundary constraint command
set_db place_hard_fence true
set_db opt_honor_fences true
create_boundary_constraint -type fence -rects {129.00500 199.15800 255.34550 75.32550} -hinst core_i/ex_stage_i
Sanity Checks | 
Verify command | Results
check_place | Placed = 21579 Unplaced = 0
report_timing -pre_cts | Wns -5.139ns (reg-reg)
Placement
Module instance count | 
Inst name | Inst Count
id_stage_i | 6627
ex_stage_i | 5321
cs_register_i | 2258
If_stage_i | 1503
Load_store_unit | 653
Placement is the step in the design process where standard cells are placed on the core boundary.
08
Notes: I have placed this module in the specific area because this is optimal place for module to be placed because this will not coming the way other module and their respective pins while maintaining the connection with other module without barrier. I have used boundary constrain command is

## Slide 9
Clock Tree Synthesis
Fig : Clock tree window
09
Clock tree synthesis is the process of creating this clock path from clock source to clock sinks. All clock pins of flip flop are considered as clock sinks (leaf) where the clock tree synthesis ends
trunk
leaf
Clock tree synthesis command
ccopt_design
opt_design –post_cts -hold
Notes: In this stage ideal clock converts to clock tree synthesis and creating this clock path from clock source to clock sinks. I have used in this command ccopt_design for build in a clock tree. And also uesd opt_design command purpose of hold timing optimization before cts. This picture is clock tree synthesis for my design and clock is propagated and we can see these are trunk and these are leaf.

## Slide 10
Clock Tree Synthesis
Non Default Rules (NDR)
NDRs make the clock routes less sensitive to crosstalk
Double/triple width for avoiding electromigration
Double/triple width for avoiding crosstalk
Fig : Metal2 is used for the Leaf
Fig : Metal4 is used for the Trunk
create_route_rule -name cts_2x_space_2x_width
-spacing_multiplier “Metal3:Metal4 2”
-width_multiplier “Metal3:Metal4 2”
create_route_type -name cts_trunk
route_rule cts_2x_space_2x_width
Create route rule command
Execute command
10
Notes: I have applied NDR for avoiding crosstalk and electromigration. I have used in this command for route rule and this command used for route rule execute.i have created NDR rule 2x space and 2x width for metal4 which is trunk. And similar command used for meat2 which is leaf just changed NDR. Where space is 2x and width is 1x.

## Slide 11
11
CTS Routing Rules
Shielding
Non Default Rules (NDR)
Metal4
Shield VSS
Clock Tree Synthesis
Shielding command
create_route_type -name cts_trunk -shield_net VSS
Fig : Metal4 shielding window
Timing Report | 
Setup | -0.928ns (reg-reg)wns
Hold | -0.182ns (reg-reg)wns

## Slide 12
set_route_attributes -nets * -avoid_detour true
12
Detouring using command
Routing
Making physical connection between signal pins using metal layer are called routing.
Route
NanoRoute
Specify Attribute
Route Attribute window
Net Attribute
Avoid Detour
True
Detouring using GUI mode
Fig : Detouring off
Fig : Detouring on

## Slide 13
Timing Reports | 
Setup | - 4.684ns (reg-reg) wns
Hold | - 0.184ns (reg-cgate) wns
Routing Congestion
Routing Congestion Reports |  |  | 
 | Hotspot Score | Max Hotspot (worst) | Top Routing layer
Before partial blockage | 690 | 467 (Metal2) | Metal4
Before partial blockage | 548 | 419 (Metal4) | Metal5
After partial blockage | 468 | 514 (Metal4) | Metal5
Power stripe density 15% | 225 | 74 (Metal2) | Metal5
Fig : Before partial blockage
Fig : After partial blockage
create_route_blockage -rects {27.36 13.68 205.19 157.31} -partial 70 -layers {Metal2 Metal4}
Routing partial blockage command
13

## Slide 14
14
View: Setup WNS ALL -1.118
Group : in2out -0.135
Group : in2reg -0.330
Group : reg2cgate 0.000
Group : reg2out -1.118
Group : reg2reg -0.700
Group : Default 0.037
View: Hold WNS
ALL -0.189
Group : in2out 0.690
Group : in2reg -0.042
Group : reg2cgate -0.189
Group : reg2out 0.400
Group : reg2reg -0.184
Group : Default -0.077
Postroute
Timing report
Command : time_design –post_route
Command : time_design –post_route -hold
Sanity Check | 
Verify commnad | Results
check_drc | Metspc -395 Short -1 Total -396
check_place | Placed -24387 Density without filler -92.73% Density with filler -100%
check_connectivity | Zero violation
Timing optimization
Design Rule Constrains clean
Design Rule violation fixing
Timing optimization command
Opt_design –post_route
Opt_design –post_route -hold

## Slide 15
Setup & Hold Timing Fixed
Reduced the frequency to 350MHz
Set new input delay is 0.2857ns which is 10% of the period
Set new output delay is 0.5714ns which is 20% of the period
Command used is opt_design –postroute –setup
15
Used Method
Fig : Setup timing results
Fig : Hold timing results

## Slide 16
edit_update_via -area {x1 x2 y1 y2} -from M2_M1_1 -to M2_M1_2x1_HH_C
MetSpec fixed command
delete_routes -regular_wire_with_drc
route_eco -fix_drc
Metal Short fixed command
17
DRC Result = zero violation
Design Rule Check
Verify DRC | 
Verify Command | Results
check_drc | MetSpec – 395 Short - 1
Violation_browser
Error position in the design
From Via selected
Replace via
To via selected
check_drc –view_window
result

## Slide 17
18
Cells are bounded within the selected region
Routing congestion even after applying partial blockage
Meeting setup and hold timing violations
Multiple DRC Fixing
Challenges

## Slide 18
Thank You